## Slide 1: Network+ Guide to Networks
Chapter 10
TCP/IP and Subnetting

## Slide 2: IPv4 Addressing
IP address information
  Network Class determined by first octet
    Class A, Class B, Class C
Table 4-1 Commonly used TCP/IP classes

## Slide 3: IPv4 Addressing

## Slide 4: IPv4 Addressing (cont’d.)
Class A devices
  Share same first octet (bits 0-7) as Network ID
  Host: second through fourth octets (bits 8-31)
Class B devices
  Share same first two octet (bits 0-15): Network ID
  Host: second through fourth octets (bits 16-31)
Class C devices
  Share same first three octet (bits 0-23): Network ID
  Host: second through fourth octets (bits 24-31)

## Slide 5: IP Address - Special Cases
127.0.0.0 network is called the loopback address
Loopback test
  Attempting to connect to own machine
  Powerful troubleshooting tool
IETF reserved addresses for private networks
  Class A addresses beginning with 10
  Class B addresses from 172.16 to 172.31
  Class C addresses from 192.168.0 to 192.168.255
  These addresses can’t be routed across the Internet

## Slide 6: Binary and Dotted Decimal Notation
Decimal number between 0 and 255 represents each binary octet
Period (dot) separates each decimal
Dotted decimal address has binary equivalent
  Converting each octet
  Remove decimal points

## Slide 7
Subnetting
  Subdividing network single class into multiple, smaller logical networks (segments)
    Control network traffic
    Make best use of limited number of IP addresses
  Subnet mask varies depending on subnetting
Nonsubnetted networks use defaults
Table 4-2 Default subnet masks

## Slide 8: Subnetting
Separates network
  Multiple logically defined segments (subnets)
    Geographic locations, departmental boundaries, technology types
Subnet traffic separated from other subnet traffic
Reasons to separate traffic
  Enhance security
  Improve performance
  Simplify troubleshooting

## Slide 9: Classful Addressing in IPv4
First, simplest IPv4 addressing type
Adheres to network class distinctions
Recognizes Class A, B, C addresses
Figure 4-8 IP addresses and their classes

## Slide 10: Classful Addressing in IPv4 (cont’d.)
Network information (network ID)
  First 8 bits in Class A address
  First 16 bits in Class B address
  First 24 bits in a Class C address
Host information
  Last 24 bits in Class A address
  Last 16 bits in Class B address
  Last 8 bits in Class C address

## Slide 11: Classful Addressing in IPv4 (cont’d.)
Figure 10-1 Example IPv4 addresses with classful addressing

## Slide 12: Classful Addressing in IPv4 (cont’d.)
Drawbacks
  Fixed network ID size limits number of network hosts
  Difficult to separate traffic from various parts of a network

## Slide 13: IPv4 Subnet Masks
Identifies how network subdivided
Indicates where network information located
Subnet mask bits
  1: corresponding IPv4 address bits contain network information
  0: corresponding IPv4 address bits contain host information

## Slide 14: IPv4 Subnet Masks (cont’d.)
Default subnet mask uses a 255 in each octet of the address that corresponds to the network portion and a zero in each octet that corresponds to the host portion.
Table 10-1 Default IPv4 subnet masks

## Slide 15: Reserved Addresses
Cannot be assigned to node network interface; used as subnet masks
Network ID
  Bits available for host information set to 0
  Classful IPv4 addressing network ID ends with 0 octet
  Subnetting allows network ID with other decimal values in last octet(s)
Broadcast address
  Octet(s) representing host information equal all 1s
  Decimal notation: 255

## Slide 16: IPv4 Subnetting Techniques
Subnetting breaks classful IPv4 addressing rules
  IP address bits representing host information change to represent network information
    Reduce usable host addresses per subnet
    Hosts, subnets available after subnetting related to host information bits borrowed

## Slide 17: IPv4 Subnetting Techniques (cont’d.)
Table 10-3 IPv4 Class B subnet masks

## Slide 18: IPv4 Subnetting Techniques (cont’d.)
Class C network
  Fewer subnets than Class B
  Same number of hosts per subnet as Class B
Table 10-4 IPv4 Class C subnet masks

## Slide 19: Calculating IPv4 Subnets
Formula: 2n −2=Y
  n: number of subnet mask bits needed to switch
    From 0 to 1
  Y: number of resulting subnets
Example
  Class C network
    Network ID: 199.34.89.0
    Want to divide into six subnets

## Slide 20: Calculating IPv4 Subnets (cont’d.)
Table 10-5 Subnet information for six subnets in an example IPv4 Class C network

## Slide 21: Calculating IPv4 Subnets (cont’d.)
Class A, Class B, and Class C networks
  All can be subnetted
    Each class has different number of host information bits usable for subnet information
    Varies depending on network class and the way subnetting is used
LAN subnetting
  LAN’s devices interpret device subnetting information
  External routers need network portion of device IP address

## Slide 22
Figure 10-3 A router connecting several subnets

## Slide 23: Calculating Supernets
Supernetting “borrows” bits from network portion of an IP address to “lend” those bits to host portion
  Permits consecutive IP network addresses to be combined and viewed in a single logical network
Combining two or more small networks into one larger network is only one reason to supernet
  Supernetting can combine multiple routing table entries into a single entry, which can drastically decrease the table’s size on Internet routers
  This reduction in routing table size increases the speed and efficiency of Internet routers
Notes: Say you have three class C network addresses 192.168.0.0 192.168.1.0 192.168.2.0 and 192.168.3.0
You have 900 hosts on the network
Combine the 4 networks by borrowing bits from the network side to combine the networks need 2 bits (2^2 = 4)
192.168.0.0 as network address with subnet 255.255.252.0 (255.255.11111100.0)
Now you have 10 bits for the host portion instead of 8 so number of hosts = 2^10 – 2 = 1022 so you can have 900 hosts on the network
Routing table == table of networks Internet routers can have huge routing table
Supernetting combines multiple routing table entries into one so reduces search time and table size

## Slide 24: CIDR (cont’d.)
Figure 10-4 Subnet mask and supernet mask

## Slide 25: CIDR Notation
CIDR notation (or slash notation)
  Shorthand denoting subnet boundary position
  Form
    Network ID followed by forward slash ( / ), followed by number of bits used for extended network prefix
    i.e. CIDR of 192.168.100.0/26 would indicate a class C subnetted address using 26 bits for the network address and thus only 6 for the host.
  CIDR block
    Forward slash, plus number of bits used for extended network prefix

## Slide 26: Network Address Translation (NAT)
Notes: Sub and super netting helps alleviate, but simply are more efficient use of IP addresses
NAT allows an organization to have their own private IP addresses while connected to the internet
Same IP addresses within the company
Only need public IP address when going to world…reduces number of public IP addresses dramatically
Also PAT (Port Address Translation) that uses port numbers and shares a single IP address; send the port address with the request and the PAT table takes care of setting up the proper address (ports 1024 to 65535)

## Slide 27: Internet Protocol Version 6 (IPv6)
IPv6 solves several IPv4 problems
  Limiting 32-bit address space
    An IPv6 address is 128 bits long
  Lack of built-in security
    IPSec provides authentication and encryption
  A sometimes complicated setup
    IPv6 is autoconfiguring (stateless or stateful)
  Lack of built-in QoS
    QoS headers in IPv6 packets can identify packets that require special or priority handling, making applications such as streaming audio and video much easier to implement

## Slide 28: IPv6
IPv6 uses a 128-bit address, allowing for 2128, or approximately 3.4×1038 addresses, or more than 7.9×1028 times as many as IPv4, which uses 32-bit addresses.
IPv4 allows for only approximately 4.3 billion addresses.
The two protocols are not designed to be interoperable, complicating the transition to IPv6.
IPv6 addresses consist of eight groups of four hexadecimal digits separated by colons, for example 2001:0db8:85a3:0042:1000:8a2e:0370:7334

## Slide 29: IPv6 Addresses
IPv6 address notation:
  Longhand notation: 2001:260:0:0:0:2ed3:340:ab
  Shorthand notation: 2001:260::2ed3:340:ab
    If one of the 16-bit numbers doesn’t require four hexadecimal digits, the leading 0s are omitted
  Addresses have a three-part addressing hierarchy
    A public topology (first three 16-bit sections)
    A site topology (next 16 bits)
    An interface identifier (last 64 bits)
      Derived from the MAC address on the host’s NIC