## Slide 1: Introduction to Networking and Networking Concepts
Chapter 1
420-A32 Networks

## Slide 2: What is a Network?
Something resembling an openwork fabric or structure in form or concept, especially:
  A system of lines or channels that interconnect a group
  A complex, interconnected group or system
  An extended group of people with similar interests or concerns who interact and remain in informal contact for mutual assistance or support
  A system of electric components and connecting circuitry designed to function in a specific manner.
  A system of computers interconnected by wires or other means in order to share information.

## Slide 3: What is Computer Networking?
Connecting computers and other electronic devices together
A great deal of technology is required for one device to connect and communicate with another, and many choices for physical connections and related software are possible
An elementary network consists of two computers connected by some kind of transmission medium

## Slide 4: Why Use Networks?
To share data and to communicate quickly and efficiently
  Sharing enables users to exchange information and route data between them as workflow demands
  Can improve human communication substantially
  Peripheral device sharing enables users to take advantage of peripherals and other devices attached directly to a network or to a generally available computer attached to a network

## Slide 5: Why Use Networks?
Network admin can centrally control the network and the clients on it
Security is enhanced and more easily controlled:
  Users can be assigned different privileges depending on their job function.
  Security of files more easily controlled than if they are kept on the client systems distributed all over the network.
  Network restricts access to unwanted users and hackers.

## Slide 6: Why Use Networks?
Programs can be located on the network and shared by all the users.
  This makes it easier to ensure all users are using the same version of the software.
  Updating the software is easier and cheaper
  Users can share the programs data files which allows them to participate in group work even at great distances.
  Data backup and restore much easier than if the files are distributed on the client machines.

## Slide 7: Why Use Networks?
Devices can be shared on the network meaning:
  Fewer devices are required
  Users have access to better devices than they could afford individual
  Services of devices can be more centrally located
  Updating of devices and device drivers more easily maintained

## Slide 8: Network Medium
To communicate successfully, computers must share access to a common network medium
  Its job is to carry the signals one computer sends to one or more other computers
Computers must attach to the network medium by using some kind of physical interface
  Network interface card (NIC) or network adapter
For large-scale networks, multiple media usually work together (interoperate) across the total networking environment

## Slide 9: Network Protocol
Network protocol: common set of rules that allows two computers on a network to communicate with one another successfully
  How to interpret signals, how to identify a computer on a network, how to initiate and end networked communications, and how to manage information exchange across the network medium
Examples:
  TCP/IP
  NetBEUI
  IPX/SPX

## Slide 10: Network Software
Computers need network software to issue the requests and responses that let them take the roles of clients and servers
Network operating system (NOS): determines what services that computer can offer or request
  Controls access to network services and network resources a computer makes available to clients
With today’s operating systems, the line between a client and a server has become blurred
  However, most operating systems have a workstation version and a server version.

## Slide 11: Network Services
Sharing resources and communication requires two components:
  server component that provides access to resource
  client component that requests access to resource
Both components are referred to as a service
NOSs must be outfitted with the types of services your client operating systems require
  web servers
  e-mail servers
  file and print servers

## Slide 12: Common Network Elements
Client
  Network computer requesting resources or services from another network computer
  Client workstation human user
  Client software installed on workstation
Server
  Network computer managing shared resources
  Runs network operating system
Workstation
  Personal computer
    May or may not be connected to network

## Slide 13: Common Network Elements
NIC (network interface card)
  Device inside computer
    Connects computer to network media
    Allows communication with other computers

## Slide 14: Network Interface Card (NIC)

## Slide 15: Terminology
Host
  Computer
    Enables network resource sharing by other computers
Node
  Client, server, or other device
    Communicates over a network
    Identified by unique number (network address)
Connectivity device
  Allows multiple networks or multiple parts of one network to connect and exchange data

## Slide 16: Terminology
Segment
  Group of nodes
    Use same communications channel for traffic
Backbone
  Connects segments and significant shared devices
  “A network of networks”
Topology
  Computer network physical layout
  Ring, bus, star or hybrid formation

## Slide 17: Common Network Terms
Protocol
  Standard method or format for communication between networked devices
Data packets
  Distinct data units exchanged between nodes
Addressing
  Scheme for assigning unique identifying number to every node
Transmission media
  Means through which data is transmitted and received

## Slide 18: Transmission Media

## Slide 19: How Networks Are Used
Network services
  Functions provided by a network
  Most visible one is e-mail
  Other vital services
    Printer sharing
    File sharing
    Internet access and Web site delivery
    remote access capabilities
    provision of voice (telephone) and video services
    network management

## Slide 20: File and Print Services
File services
  Capability of server to share data files, applications and disk storage space
File server
  Provides file services
File services provide foundation of networking
Print services
  Share printers across network
  Saves time and money

## Slide 21: Access Services
Allow remote user network connection
Allow network users to connect to machines outside the network
Remote user is a computer user on different network or in different geographical location
Network operating systems include built-in access services
Allow external users to use network resources and devices
  Same as if logged on to office workstation

## Slide 22: Communications Services
Convergence
  Phenomenon of offering multiple types of communications services on the same network
Unified communications
  Multiple network-based communications centralized management
E-mail
  Oldest and most frequently used
Mail server
  Computer responsible for mail services
    Coordinates storage and transfer of e-mail

## Slide 23: Communications Services
Additional tasks of mail servers
  Intercept spam
  Handle objectionable content
  Route messages according to rules
  Provide Web-based client
  Notify administrators or users if certain events occur
  Schedule e-mail transmission, retrieval, storage, maintenance functions
  Communicate with mail servers on other networks
Mail server runs specialized mail server software

## Slide 24: Internet Services
Supplying Web pages
  Servers work together to bring Web pages to user’s desktop
  Web server
    Computer installed with appropriate software to supply Web pages to many different clients upon demand
Other Internet services
  File transfer capabilities, Internet addressing schemes, security filters, means for directly logging on to other Internet computers

## Slide 25: Management Services
Small network management
  Single network administrator
  Network operating system’s internal functions
Today’s larger network management
  Centrally administered network management tasks

## Slide 26: Management Services
Other important services
  Traffic monitoring and control
  Load balancing
  Hardware diagnosis and failure alert
  Asset management
  License tracking
  Security auditing
  Address management
  Backup and restoration of data

## Slide 27: A Simple Network

## Slide 28: Understanding Network Types
Networks fall into two major types: peer-to-peer and client/server (also called server-based)
This discussion of network types addresses the roles that computers play on the network and how those roles interact
Client/server networks are the most typical and represent the primary focus of the discussion here
Understanding both types is essential, especially as they compare with one another

## Slide 29: Peer-to-Peer Networks
In a peer-to-peer network, every user must also act as a network administrator, controlling access to the resources on their machines
Because of this flexibility, institutionalized chaos is the norm for peer-to-peer networks
  Security can be a major concern
  Computers can be affiliated into loose federations called workgroups, but no network-wide security can be enforced
  As the number of users and resources grows, these networks can become unworkable

## Slide 30: Peer-to-Peer Networks
Resource sharing on a simple peer-to-peer network

## Slide 31: Peer-to-Peer Networks

## Slide 32: Peer-to-Peer Advantages
Easy to install and configure
Machines don’t depend on the presence of a dedicated server
Users control their own shared resources
Inexpensive to purchase and operate
Need no additional equipment or software beyond a suitable operating system
No dedicated administrators are needed
Work best for networks with 10 or fewer users

## Slide 33: Peer-to-Peer Disadvantages
Not secure
Users might be forced to use as many passwords as there are shared resources
Each PC must be backed up to protect shared data
When a shared resource is accessed, performance of the PC where the resource resides is reduced
There is no centralized organizational scheme to locate or control access to data
Access to a shared resource is unavailable if PC where resource resides is turned off/crashes
Doesn’t usually work well with more than 10 users

## Slide 34: Peer-to-Peer Networks
Resource sharing method
  Modify file sharing controls
    A user responsibility
  Not centrally controlled
    Potential variations and security issues
Environments
  Small home or office
  Large networks using the Internet
    Gnutella, Freenet, original Napster
    BitTorrent software

## Slide 35: Client/Server Networks

## Slide 36: Client/Server Networks
Central computer (server)
  Facilitates communication and resource sharing
Clients (other computers)
  Personal computers
    Known as workstations
Central resource sharing controlled by server
  Data sharing, data storage space, devices
  No direct sharing of client resources

## Slide 37: Client/Server Networks
Computer roles
  Server
  Clients
    Run local applications
    Store data locally
    Use server shared applications, data, devices
    Use server as intermediary
Communication
  Switches or routers

## Slide 38: Client/Server Networks
Resource sharing on a client/server network

## Slide 39: Client/Server Networks
Server requirement - Network operating system
  Manages client data, resources
  Ensures authorized user access
  Controls user file access
  Restricts user network access
  Dictates computer communication rules
  Supplies application to clients

## Slide 40: Client/Server Networks
Server examples
  UNIX
  Linux
  Microsoft Server 2003 and 2008
  MAC OS X Server
Server features relative to clients
  More memory, processing, storage capacity
  Equipped with special hardware
    Provides network management functions

## Slide 41: Client/Server Advantages
Advantages relative to peer-to-peer networks
  Centralized user accounts, security, and access controls simplify network administration
  Multiple shared resource access centrally controlled
  Central problem monitoring, diagnostics capabilities
  More powerful equipment means more efficient access to network resources
  User response time optimization capabilities
  Efficient processing on large networks
  Scalability
Popular in medium- and large-scale organizations

## Slide 42: Client/Server Disadvantages
At the worst, server failure renders a network unusable; at the least, it results in loss of network resources
Complex server software requires allocating expert staff, which increases expenses
Dedicated hardware and specialized software add to the cost of server-based networking

## Slide 43: The Role of Network Servers
The server is at the heart of any network that’s too large for a peer-to-peer configuration
Most large networks with more than a few dozen workstations rely on several network servers
Your knowledge of a server’s unique hardware requirements and the many roles it can play in a network is essential to being able to design and support today’s computer networks

## Slide 44: Application Servers
Application servers supply the server side of client/server applications, and often the data that goes along with them, to network clients
  For example, a database server
  Differ from basic file and print servers by providing processing services as well as handling requests for file or print services

## Slide 45: Communication Servers
Communication servers provide a mechanism for users outside a network to access that network’s resources, and sometimes permit users on a network to access resources outside network’s local scope
  Often, installing communication servers on a network enables users who are traveling or working at home to dial in to the network via a modem
    In Windows Server 2000/2003: Routing and Remote Access Service (RRAS)

## Slide 46: File and Print Servers
File and print servers provide basic network file storage, retrieval services, and access to networked printers
  Users can run applications locally but keep data files on the server (and print those files when they want hard copies)
  Any Windows, NetWare, or Linux server can act as a file and print server

## Slide 47: Mail Servers
Mail servers handle e-mail messages for users
  Might involve simply acting as a clearinghouse for local exchange of messages
  Also commonly provide “store-and-forward” services
  Can store outgoing messages until a connection to an external mail server is established, and then forward messages to their intended destinations
  Examples: Microsoft Exchange Server, GroupWise, and Lotus Notes

## Slide 48: Web Servers
The World Wide Web is the most well-known aspect of the Internet, made up of documents that can be interlinked by using hyperlinks
  Examples: Internet Information Services (IIS), Apache Web server
    Apache is the most widely used Web server in the world
  Many organizational intranets take advantage of free Web server packages

## Slide 49: LANs, MANs, and WANs
LAN (local area network)
  Network confined to a relatively small space
  1980s
    LANs became popular as peer-to-peer based
  Today
    Larger and more complex client/server network
MAN (metropolitan area network)
  Network extends beyond building boundaries
  Larger than LAN
  Connects clients and servers from multiple buildings

## Slide 50: LANs, MANs, and WANs
Figure 1-3 A more complex client/server network

## Slide 51: LANs, MANs, and WANs
WAN (wide area network)
  Connects two or more geographically distinct LANs or MANs
  Comparison to LANs
    Use slightly different transmission methods and media
    Use greater variety of technologies
  Network connection
    Separate offices in same organization
    Separate offices in different organizations

## Slide 52: A Simple WAN

## Slide 53: LAN Backbone

## Slide 54: Selecting the Right Type of Network
You have a number of choices to make when deciding how to design and implement a network
  Will a single LAN do, or is an internetwork required?
  Will peer-to-peer networking suffice, or is a server-based network in order?
  Do some functions need to be server-based while others work well as a peer-to-peer network?

## Slide 55: Choosing a LAN or an Internetwork?
Decision to design a LAN or an internetwork is based on:
  How many computers will participate on the network?
  Is there a need to tie groups of computers together with network devices such as routers?
Distance the network will span also plays a part in the decision
  A LAN is usually called for when:
    The number of computers is fewer than 100
    Network use and security factors don’t require a router
    The network is confined to a single building or floor

## Slide 56: Choosing Peer-to-Peer or Client/Server
Choosing peer-to-peer networking exclusively is appropriate only when all the following hold:
  The network includes no more than 10 users
  All networked machines are close enough to fit within the span of a single LAN
  Budget considerations are paramount
  No specialized servers are needed

## Slide 57: Choosing Peer-to-Peer or Client/Server
A client/server network makes sense when one or more of the following conditions is true:
  More than 10 users must share network access
  Centralized control, security, resource management, or backup is desirable
  Users need access to specialized servers, or they place heavy demands on network resources
  An internetwork is in use
Hybrid network uses elements of both a client/server network and a peer-to-peer network

## Slide 58: Unintelligent Network
Notes: Intelligence is in the data that is moving on the network. The data has to know where it is going in order to get to the right spot

## Slide 59: Intelligent Network
Notes: In an intelligent network parts of the network know where things go and they take care of making sure things go where they are supposed to