## Slide 1: IP Addressing Summary

## Slide 2: IPv4 Addressing
Networks recognize two addresses
  Logical (Network layer)
  Physical (MAC, hardware) addresses
IP protocol handles logical addressing
Specific parameters – IPv4
  Unique 32-bit number
    Divided into four octets (sets of eight bits)
    Separated by periods
Example: 144.92.43.178

## Slide 3: IPv4 Addressing (cont’d.)
IP address information
  Class A - Network address determined by first octet
  Class B – Network address determined by first 2 octets
  Class C – Network address determined by first 3 octets
  In each case the octets unused for the network address determine the client address.
Table 4-1 Commonly used TCP/IP classes

## Slide 4: IPv4 Addressing (cont’d.)
Class D, Class E rarely used (never assign)
  Class D: value between 224 and 230
    Multicasting
  Class E: value between 240 and 254
    Experimental use
Eight bits have 256 combinations
  Networks use 1 through 254
  0: reserved as placeholder
    10.0.0.0
  255: reserved for broadcast transmission
    10.0.0.255

## Slide 5: IPv4 Addressing (cont’d.)
Class A devices
  Share same first octet (bits 0-7) - Network ID
  Host: second through fourth octets (bits 8-31)
Class B devices
  Share same first two octet (bits 0-15) - Network ID
  Host: third and fourth octets (bits 16-31)
Class C devices
  Share same first three octet (bits 0-23) - Network ID
  Host: fourth octet (bits 24-31)

## Slide 6
Figure 4-8 IP addresses and their classes

## Slide 7: IPv4 Addressing (cont’d.)
Loop back address
  First octet equals 127 (127.0.0.1)
Loopback test
  Attempting to connect to own machine
  Powerful troubleshooting tool
    Indicates that your NIC and networking software is working
Windows
  ipconfig command
  For more information use ipconfig /all
Unix, Linux
  ifconfig command
  May have to be installed first

## Slide 8: IPv4 Addressing (cont’d.)
Figure 4-9 Results of the ipconfig /all command on a Windows workstation. Physical address is the MAC address of the adapter.

## Slide 9: IPv4 Addressing (cont’d.)
Figure 4-10 Results of the ifconfig -a command on a UNIX workstation. Hwaddr is the MAC address of the network adapter

## Slide 10: Binary and Dotted Decimal Notation
Decimal number between 0 and 255 represents each binary octet
Period (dot) separates each decimal
Dotted decimal address has binary equivalent
  Converting each octet
  Remove decimal points

## Slide 11: Subnet Mask
Identifies every device on TCP/IP-based network
32-bit number (net mask)
  Identifies device’s subnet
    Combines with device IP address
    Informs network about segment, network where device attached
Four octets (32 bits)
  Expressed in binary or dotted decimal notation
Assigned same way a IP addresses
  Manually, automatically (via DHCP)

## Slide 12
For a given default subnet mask you must adhere to the beginning octet range for that network.
i.e. Class A networks must start with a value between 1-126, B between 128 – 191 and C between 192-223.
Table 4-2 Default subnet masks

## Slide 13: Automatic Private IP Addressing
A feature of Microsoft Windows, APIPA is a DHCP failover mechanism for local networks. With APIPA, DHCP clients can obtain IP addresses when DHCP servers are non-functional. APIPA exists in all modern versions of Windows except Windows NT.
When a DHCP server fails, APIPA allocates IP addresses in the private range 169.254.0.1 to 169.254.255.254.
In APIPA, all devices reside on the same Class B subnet.

## Slide 14: APIPA (cont’d.)
APIPA
  Assigns computer’s network adapter IP address from the pool
  Assigns subnet default Class B network
    255.255.0.0
  Part of operating system
    No need to register; check with central authority
Disadvantage
  Computer only communicates with other nodes using addresses in APIPA range

## Slide 15: APIPA (cont’d.)
APIPA suitable use
  Small networks: no DHCP servers
APIPA unsuitable use
  Networks communicating with other subnets, WAN
APIPA enabled by default
  First checks for DHCP server
    Allows DHCP server to assign addresses
  Does not reassign new address if static
  Can be disabled in registry

## Slide 16: Automatic Private IP Addressing
This can sometimes be a valuable tool when debugging network configuration problems.
  If you have a Windows automatic IP address instead of the address you expect from your DHCP server then you are having a connection problem back to the network’s DHCP server.
  This can be caused by many things, but the first thing to check is all the cabling back from the Host to the server to see if there are any problems.
Also check to make sure that your computer is set to receive automatic IP addresses and is not manually setting the IP address to a range outside your server’s subnet.

## Slide 17: Assigning IP Addresses
Routers and servers can give IP addresses to their hosts.
Switches, hubs and crossover cables cannot.
If you are connected only by a switch, hub or crossover cable then you should expect a windows automatic IP address.
If you are connected to a router or server then you should expect the IP address as dictated in the admin panel of the router or server.
We will look at this admin panel in the next lab.

## Slide 18: Assigning IP Addresses (cont’d.)
Static IP address
  Assignment manually
  Modify client workstation TCP/IP properties
    Only way to change
  Human error cause duplicates
Automatic IP addressing
  BOOTP and DHCP
  Reduce duplication error

## Slide 19: DHCP Leasing
Device borrows (leases) IP address
  Devices use IP address temporarily
    Specified time limit
Lease time
  Determined when client obtains IP address at log on
  User may force lease termination

## Slide 20: PING (Packet Internet Groper)
Provides verification
  TCP/IP installed, bound to NIC, configured correctly, communicating with network
  Host responding
Uses ICMP services
  Send echo request and echo reply messages
    Determine IP address validity
Ping IP address or host name
Ping loopback address: 127.0.0.1
  Determine if workstation’s TCP/IP services running

## Slide 21: PING (cont’d.)
Operating system determines Ping command options, switches, syntax
Figure 4-17 Output from successful and unsuccessful PING tests