## Slide 1: Network+ Guide to Networks 5th Edition
Chapter 3
Transmission Basics and Networking Media

## Slide 2: Objectives
Explain basic data transmission concepts, including full duplexing, attenuation, latency, and noise
Describe the physical characteristics of coaxial cable, STP, UTP, and fiber-optic media
Compare the benefits and limitations of different networking media
Explain the principles behind and uses for serial connector cables
Identify wiring standards and the best practices for cabling buildings and work areas

## Slide 3: Network connections
A few slides about connecting network devices together
Cross-over versus straight-through cables

## Slide 4: Port Types
Devices on the network are divided into two types:
  MDI ports include computer NIC and the Router ports.
  MDIX ports include ports of Switch, hub or bridge.

## Slide 5: Cross-over versus straight-through cables
Cross-over cables switch the send and receive wires on each end of the cable so that two devices using similar ports can communicate.
Straight-through or patch cables connect the same wires on each side of the cable.
Generally we want to connect similar ports together with crossover cables and opposing ports together with straight-through cables.

## Slide 6: Auto-MDIX
Auto-MDIX is a technology developed by HP by Dan Dove and Bruce Melvin.
This technique allows the device to auto-detect the cable type being used and change its port type from MDI to MDIX as required so that it can properly connect using that cable.
To use this, one of the devices must have Auto-MDIX enabled and the connection speed must be set to auto.

## Slide 7: Auto-MDIX
Therefore, you must verify this before attempting to connect devices using this technology.
If you have doubts about the equipment or the setup, then using the proper cabling is still the recommended strategy to avoid possible connection problems.

## Slide 8: Transmission Basics
Chapter 3

## Slide 9: Transmission Basics
Transmit
  Issue signals along network medium
Transmission
  Process of transmitting
  Signal progress after transmitted
Transceiver
  Transmit and receive signals

## Slide 10: Analog and Digital Signaling
Important data transmission characteristic
  Signaling type: analog or digital
Volt
  Electrical current pressure
Electrical signal strength
  Directly proportional to voltage
  Signal voltage
Signals
  Current, light pulses, electromagnetic waves

## Slide 11
Analog data signals
  Voltage varies continuously
  Properties
    Amplitude, frequency, wavelength, phase
Figure 3-1: An example of an analog signal

## Slide 12: Analog and Digital Signaling (cont’d.)
Amplitude
  Analog wave’s strength
Frequency
  Number of times amplitude cycles over fixed time period
  Measure in hertz (Hz)
Wavelength
  Distance between corresponding wave cycle points
  Inversely proportional to frequency
  Expressed in meters or feet

## Slide 13
Phase
  Wave’s progress over time in relationship to fixed point
Figure 3-2: Waves with a 90-degree phase difference

## Slide 14: Analog and Digital Signaling (cont’d.)
Analog signal benefit over digital
  More variable
    Convey greater information with less energy
Drawback of analog signals
  Varied and imprecise voltage
    Susceptible to transmission flaws
Digital signals
  Pulses of voltages
    Positive voltage represents a 1
    Zero voltage represents a 0

## Slide 15
Binary system
  1s and 0s represent information
Bit (binary digit)
  Possible values: 1 or 0
  Digital signal pulse
Figure 3-3 An example of a digital signal

## Slide 16
Byte
  Eight bits together
Computers read and write information
  Using bits and bytes
Find decimal value of a bit
  Multiply the 1 or 0 by 2x (x equals bit’s position)
Figure 3-4 Components of a byte

## Slide 17: Analog and Digital Signaling (cont’d.)
Convert byte to decimal number
  Determine value represented by each bit
  Add values
Convert decimal number to a byte
  Reverse the process
Convert between binary and decimal
  By hand or calculator

## Slide 18: Analog and Digital Signaling (cont’d.)
Digital signal benefit over analog signal
  More reliable
  Less severe noise interference
Digital signal drawback
  Many pulses required to transmit same information
Overhead
  Nondata information
    Required for proper signal routing and interpretation

## Slide 19: Data Modulation
Data relies on digital transmission
Network connection may handle only analog signals
Modem
  Accomplishes translation
  Modulator/demodulator
Data modulation
  Technology modifying analog signals
  Make data suitable for carrying over communication path

## Slide 20: Data Modulation (cont’d.)
Carrier wave
  Combined with another analog signal
  Produces unique signal
    Transmitted from one node to another
  Preset properties
  Purpose
    Convey information
Information wave (data wave)
  Added to carrier wave
  Modifies one carrier wave property

## Slide 21: Data Modulation (cont’d.)
Frequency modulation
  Carrier frequency modified
    By application of data signal
Amplitude modulation
  Carrier signal amplitude modified
    By application of data signal

## Slide 22
Figure 3-5 Carrier wave modified through frequency modulation

## Slide 23: Simplex, Half-Duplex, and Duplex
Simplex
  Signal transmission: one direction
Half-duplex transmission
  Signal transmission: both directions
    One at a time
  One communication channel
    Shared for multiple nodes to exchange information
Full-duplex
  Signals transmission: both directions simultaneously
  Used on data networks

## Slide 24
Channel
  Distinct communication path between nodes
  Separated physically or logically
Full duplex advantage
  Increases speed
Figure 3-6 Simplex, half-duplex, and full duplex transmission

## Slide 25: Multiplexing
Multiplexing
  Multiple signals travel simultaneously over one medium
Subchannels
  Logical multiple smaller channels
Multiplexer (mux)
  Combines many channel signals for transportation over a medium
Demultiplexer (demux)
  Separates combined signals at the destination and regenerates them

## Slide 26
TDM (time division multiplexing)
  Divides channel into multiple time intervals
Figure 3-7 Time division multiplexing

## Slide 27
Statistical multiplexing
  Transmitter assigns slots to nodes according to priority, need
  More efficient than TDM
Figure 3-8 Statistical multiplexing

## Slide 28
FDM (frequency division multiplexing)
  Unique frequency band for each communications subchannel
  Two types
    Cellular telephone transmission
    DSL Internet access
Figure 3-9 Frequency division multiplexing

## Slide 29
WDM (wavelength division multiplexing)
  One fiber-optic connection
  Carries multiple light signals simultaneously
DWDM (dense wavelength division multiplexing)
  Used on most modern fiber-optic networks
  Extraordinary capacity
Figure 3-10 Wavelength division multiplexing

## Slide 30: Relationships Between Nodes
Point-to-point transmission
  One transmitter and one receiver
Point-to-multipoint transmission
  One transmitter and multiple receivers
Broadcast transmission
  One transmitter and multiple, undefined receivers
  Used on wired and wireless networks
    Simple and quick
Nonbroadcast
  One transmitter and multiple, defined receivers

## Slide 31: Relationships Between Nodes (cont’d.)
Figure 3-11 Point-to-point versus broadcast transmission

## Slide 32: Throughput and Bandwidth
Throughput
  Measures amount of data transmitted
  During given time period
  Capacity or bandwidth
  Quantity of bits transmitted per second
Bandwidth (strict definition)
  Measures difference between highest and lowest frequencies medium can transmit
  Range of frequencies
  Measured in hertz (Hz)

## Slide 33: Throughput and Bandwidth (cont’d.)
Table 3-1 Throughput measures

## Slide 34: Common media characteristics
Chapter 3

## Slide 35: Common Media Characteristics
Selecting transmission media
  Match networking needs with media characteristics
Physical media characteristics
  Throughput
  Cost
  Size and scalability
  Connectors
  Noise immunity

## Slide 36: Network Media
Chapter 3

## Slide 37: Throughput
Most significant transmission method factor
Causes of limitations
  Laws of physics
  Signaling and multiplexing techniques
  Noise
  Devices connected to transmission medium
Fiber-optic cables allows faster throughput
  Compared to copper or wireless connections

## Slide 38: Cost
Precise costs difficult to pinpoint
Media cost dependencies
  Existing hardware, network size, labor costs
Variables influencing final cost
  Installation cost
  New infrastructure cost versus reuse
  Maintenance and support costs
  Cost of lower transmission rate affecting productivity
  Cost of obsolescence

## Slide 39: Noise Immunity
Noise distorts data signals
  Distortion rate dependent upon transmission media
    Fiber-optic: least susceptible to noise
Limit impact on network
  Cable installation
    Far away from powerful electromagnetic forces
  Select media protecting signal from noise
  Antinoise algorithms

## Slide 40: Size and Scalability
Three specifications
  Maximum nodes per segment
  Maximum segment length
  Maximum network length
Maximum nodes per segment dependency
  Attenuation and latency
Maximum segment length dependency
  Attenuation and latency plus segment type

## Slide 41: Size and Scalability (cont’d.)
Segment types
  Populated: contains end nodes
  Unpopulated: No end nodes
    Link segment
Segment length limitation
  After certain distance, signal loses strength
    Cannot be accurately interpreted

## Slide 42: Connectors and Media Converters
Connectors
  Hardware connecting wire to network device
  Specific to particular media type
  Affect costs
    Installing and maintaining network
    Ease of adding new segments or nodes
    Technical expertise required to maintain network
Media converter
  Hardware enabling networks or segments running on different media to interconnect and exchange signals

## Slide 43: Connectors and Media Converters (cont’d.)
Figure 3-15 Copper wire-to-fiber media converter

## Slide 44: Primary Cable Types
Coaxial Cable
Twisted Pair
  Unshielded Twisted Pair (UTP)
  Shielded Twisted Pair (STP)
Fiber Optics

## Slide 45: Coaxial Cable
Central metal core (often copper)
  Surrounded by insulator
Braided metal shielding (braiding or shield)
Outer cover (sheath or jacket)
Figure 3-16 Coaxial cable

## Slide 46: Coaxial Cable (cont’d.)
High noise resistance
Advantage over twisted pair cabling
  Carry signals farther before amplifier required
Disadvantage over twisted pair cabling
  More expensive
Hundreds of specifications
  RG specification number
  Differences: shielding and conducting cores
    Transmission characteristics

## Slide 47: Coaxial Cable (cont’d.)
Conducting core
  American Wire Gauge (AWG) size
Data networks usage
  RG-6
  RG-8
  RG-58
  RG-59

## Slide 48: Coaxial Cable (cont’d.)
Figure 3-17 F-type connector
Figure 3-18 BNC Connector

## Slide 49: Twisted Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
Figure 3-19 Twisted pair cable

## Slide 50: Twisted Pair Cable (cont’d.)
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation

## Slide 51: Twisted Pair Cable (cont’d.)
Hundreds of different designs
  Dependencies
    Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Twisted pair wiring types
  Cat (category) 3, 4, 5, 5e, 6, and 6e, Cat 7
  CAT 5 most often used in modern LANs

## Slide 52: Twisted Pair Cable (cont’d.)
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
  Handles current faster networking transmission rates
Two categories
  STP (shielded twisted pair)
  UTP (unshielded twisted pair)

## Slide 53: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded
Figure 3-20 STP cable

## Slide 54: UTP (Unshielded Twisted Pair)
Maximum segment length is 100 meters
Most popular form of LAN cabling
The UTP cable used for networking usually includes one or more pairs of insulated wires
UTP is used for telephony, but requirements for networking uses differ from the telephony ones

## Slide 55: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance
Figure 3-21 UTP cable

## Slide 56: UTP (Unshielded Twisted Pair) (cont’d.)
EIA/TIA standards
  Cat 3 (Category 3)
  Cat 4 (Category 4)
  Cat 5 (Category 5)
  Cat 5e (Enhanced Category 5)
  Cat 6 (Category 6)
  Cat 6e (Enhanced Category 6)
  Cat 7 (Category 7)

## Slide 57: UTP (Unshielded Twisted Pair) (cont’d.)
Figure 3-22 A Cat 5 UTP cable with pairs untwisted

## Slide 58: Comparing STP and UTP
Throughput
  STP and UTP transmit at the same rates
Cost
  STP and UTP vary
Noise immunity
  STP more noise resistant
  UTP subject to techniques to offset noise
Size and scalability
  STP and UTP maximum segment length
    100 meters

## Slide 59: Comparing STP and UTP (cont’d.)
Connector
  STP and UTP use RJ-45 (Registered Jack 45)
    8 wires in 4 pairs
  Telephone connections use RJ-11 (Registered Jack 11)
    4 wires in 2 pairs
Figure 3-23 RJ-45 and RJ-11 connectors

## Slide 60: Terminating Twisted Pair Cable
Patch cable
  Relatively short cable
  Connectors at both ends
Proper cable termination techniques
  Basic requirement for two nodes to communicate
Poor terminations
  Lead to loss or noise
TIA/EIA standards
  TIA/EIA 568A
  TIA/EIA 568B

## Slide 61
Figure 3-24 TIA/EIA 568A standard terminations
Figure 3-25 TIA/EIA 568B standard terminations

## Slide 62
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Figure 3-26 RJ-45 terminations on a crossover cable

## Slide 63: Terminating Twisted Pair Cable (cont’d.)
Termination tools
  Wire cutter
  Wire stripper
  Crimping tool
Figure 3-27 Wire cutter

## Slide 64: Terminating Twisted Pair Cable (cont’d.)
Figure 3-28 Wire stripper
Figure 3-29 Crimping tool
After making cables
  Verify data transmit and receive

## Slide 65: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One (or several) glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser
  LED (light-emitting diode) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
    Allows fiber to bend

## Slide 66: Fiber-Optic Cable (cont’d.)
Plastic buffer
  Outside cladding
  Protects cladding and core
  Opaque
    Absorbs any escaping light
Kevlar strands (polymeric fiber) surround plastic buffer
Plastic sheath covers Kevlar strands

## Slide 67
Different varieties
  Based on intended use and manufacturer
Two categories
  Single-mode
  Multimode
Figure 3-30 A fiber-optic cable

## Slide 68: SMF (Single-Mode Fiber)
Uses narrow core (< 10 microns in diameter)
  Laser generated light travels over one path
    Little reflection
  Light does not disperse
Accommodates
  Highest bandwidths, longest distances
  Connects carrier’s two facilities
Cost prohibit typical LANs, WANs use

## Slide 69: SMF (Single-Mode Fiber) (cont’d.)
Figure 3-31 Transmission over single-mode fiber-optic cable

## Slide 70: MMF (Multimode Fiber)
Uses core with larger diameter than single-mode fiber
  Common size: 62.5 microns
Laser or LED generated light pulses travel at different angles
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 71: MMF (Multimode Fiber) (cont’d.)
Figure 3-32 Transmission over multimode fiber-optic cable

## Slide 72: MMF (Multimode Fiber) (cont’d.)
Benefits
  Extremely high throughput
  Very high resistance to noise
  Excellent security
  Ability to carry signals for much longer distances before requiring repeaters than copper cable
  Industry standard for high-speed networking
Drawback
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 73: MMF (Multimode Fiber) (cont’d.)
Throughput
  Reliable transmission rates
    Can reach 100 gigabits (or 100,000 megabits) per second per channel
Cost
  Most expensive transmission medium
Connectors
  ST (straight tip)
  SC (subscriber connector or standard connector)
  LC (local connector)
  MT-RJ (mechanical transfer registered jack)

## Slide 74: MMF (Multimode Fiber) (cont’d.)
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary
    150 to 40,000 meters
    Due primarily to optical loss

## Slide 75
Figure 3-36 MT-RJ (mechanical transfer-register jack) connector
Figure 3-35 LC (local connector)
Figure 3-33 ST (straight tip) connector
Figure 3-34 SC (subscriber connector or standard connector)

## Slide 76: DTE (Data Terminal Equipment) and DCE (Data Circuit-Terminating Equipment) Connector Cables
DTE (data terminal equipment)
  Any end-user device
DCE (data circuit-terminating equipment)
  Device that processes signals
  Supplies synchronization clock signal

## Slide 77: DTE and DCE Connector Cables (cont’d.)
DTE and DCE connections are:
  Serial
    Pulses flow along single transmission line
    Sequentially
  Serial cable
    Carries serial transmissions

## Slide 78: DTE and DCE Connector Cables (cont’d.)
Figure 3-37 DB-9 connector
Figure 3-38 DB-25 connector

## Slide 79: DTE and DCE Connector Cables (cont’d.)
RS-232 (Recommended Standard 232)
  Serial ports
  EIA/TIA standard
  Physical layer specification
    Signal voltage, timing, compatible interface characteristics
  Connector types
    RJ-45, DB-9, DB-25
RS-232 connections
  Straight-through or crossover

## Slide 80: Cable Comparisons

## Slide 81: Structured Cabling
Cable plant
  Hardware making up enterprise-wide cabling system
Standard
  TIA/EIA joint 568 Commercial Building Wiring Standard

## Slide 82: Work Area
The work area is where computer workstations and other user devices are located
  Faceplates and wall jacks here and patch cables connect computers and printers to wall jacks
  Patch cables should be less than 6 meters long
  Standard calls for at least one voice and one data outlet on each faceplate in each work area
  Connection between wall jack and nearby telecommunications closet made with horizontal wiring

## Slide 83: Horizontal Wiring
Runs from the work area’s wall jack to the telecommunications closet and is usually terminated at a patch panel
Acceptable wiring types include four-pair UTP (Category 5e or 6) or two fiber-optic cables
Horizontal wiring from the wall jack to the patch panel should be no longer than 90 meters

## Slide 84: Telecommunications Closet

## Slide 85: Equipment Rooms
Houses servers, routers, switches, and other major network equipment, and serves as a connection point for backbone cabling
Can be the main cross-connect of backbone cabling for the network, or it might serve as the connecting point for backbone cabling between buildings

## Slide 86: Backbone Cabling
Interconnects TCs and equipment rooms
Runs between floors or wings of a building and between buildings
Frequently fiber-optic cable but can also be UTP

## Slide 87: Entrance Facilities
Location of the cabling and equipment that connects a corporate network to a third-party telecommunications provider
Can serve as an equipment room and the main cross-connect for all backbone cabling

## Slide 88
Figure 3-39 TIA/EIA structured cabling in an enterprise

## Slide 89
Figure 3-40 TIA/EIA structured cabling in a building

## Slide 90: Structured Cabling (cont’d.)
Components
  Entrance facilities
  MDF (main distribution frame)
  Cross-connect facilities
  IDF (intermediate distribution frame)
  Backbone wiring
  Telecommunications closet
  Horizontal wiring
  Work area

## Slide 91: Structured Cabling (cont’d.)
Table 3-2 TIA/EIA specifications for backbone cabling

## Slide 92
Figure 3-41 Patch panel
Figure 3-42 Patch panel
Figure 3-43 Horizontal wiring
Figure 3-44 A standard TIA/EIA outlet

## Slide 93: Best Practices for Cable Installation and Management
Choosing correct cabling
  Follow manufacturers’ installation guidelines
  Follow TIA/EIA standards
Network problems
  Often traced to poor cable installation techniques