## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 2
Networking Standards and the OSI Model

## Slide 2: Objectives
Identify organizations that set standards for networking
Describe the purpose of the OSI model and each of its layers
Explain specific functions belonging to each OSI model layer

## Slide 3: Objectives (cont’d.)
Understand how two network nodes communicate through the OSI model
Discuss the structure and purpose of data packets and frames
Describe the two types of addressing covered by the OSI model

## Slide 4: Networking Standards Organizations
Standard
  Documented agreement
  Technical specifications/precise criteria
  Stipulates design or performance of particular product or service
Standards are essential in the networking world
  Wide variety of hardware and software
    Ensures network design compatibility
Standards define minimum acceptable performance
  Not ideal performance

## Slide 5: Networking Standards Organizations (cont’d.)
Many different organizations oversee computer industry standards
  Organizations may overlap responsibilities
    Example: ANSI and IEEE set wireless standards
Network professional’s responsibility
  Be familiar with groups setting networking standards
  Understand critical aspects of standards required by own networks

## Slide 6: ANSI
ANSI (American National Standards Institute)
  1000+ representatives from industry and government
  Determines standards for electronics industry and other fields
Requests voluntarily compliance with standards
Obtaining ANSI approval requires rigorous testing
ANSI standards documents available online

## Slide 7: EIA
EIA (Electronic Industries Alliance)
  Trade organization
    Representatives from United States electronics manufacturing firms
  Sets standards for its members
  Helps write ANSI standards
  Lobbies for favorable computer and electronics industries legislation

## Slide 8: TIA
TIA (Telecommunications Industry Association)
  Formed in 1988
    EIA subgroup merged with former United States Telecommunications Suppliers Association (USTSA)
  Focus of TIA
    Standards for information technology, wireless, satellite, fiber optics, and telephone equipment
TIA/EIA 568-B Series
  Guidelines for installing network cable in commercial buildings

## Slide 9: IEEE
IEEE (Institute of Electrical and Electronics Engineers)
  International engineering professionals society
Goal of IEEE
  Promote development and education in electrical engineering and computer science fields
Hosts symposia, conferences, and chapter meetings
Maintains a standards board
IEEE technical papers and standards
  Highly respected

## Slide 10: ISO
ISO (International Organization for Standardization)
  Headquartered in Geneva, Switzerland
  Collection of standards organizations
    Representing 57 countries
Goal of ISO
  Establish international technological standards to facilitate global exchange of information and barrier free trade
Widespread authority

## Slide 11: ITU
ITU (International Telecommunication Union)
  Specialized United Nations agency
  Regulates international telecommunications
  Provides developing countries with technical expertise and equipment
  Founded in 1865
    Joined United Nations in 1947
  Members from 191 countries
Focus of ITU
  Global telecommunications issues
  Worldwide Internet services implementation

## Slide 12: ISOC
ISOC (Internet Society)
  Founded in 1992
  Professional membership society
  Establishes technical Internet standards
Current ISOC concerns
  Rapid Internet growth
  Keeping Internet accessible
  Information security
  Stable Internet addressing services
  Open standards

## Slide 13: ISOC (cont’d.)
ISOC oversees groups with specific missions
  IAB (Internet Architecture Board)
    Technical advisory group
    Overseeing Internet’s design and management
  IETF (Internet Engineering Task Force)
    Sets Internet system communication standards
    Particularly protocol operation and interaction
    Anyone may submit standard proposal
    Elaborate review, testing, and approval processes

## Slide 14: IANA
IP (Internet Protocol) address
  Address identifying computers in TCP/IP based (Internet) networks
  Reliance on centralized management authorities
IP address management history
  Initially: IANA (Internet Assigned Numbers Authority)
  1997: Three RIRs (Regional Internet Registries)
    ARIN (American Registry for Internet Numbers)
    APNIC (Asia Pacific Network Information Centre)
    RIPE (Réseaux IP Européens)

## Slide 15: ICANN
IP address management history (cont’d.)
  Late 1990s: ICANN (Internet Corporation for Assigned Names and Numbers)
    Private nonprofit corporation
    Remains responsible for IP addressing and domain name management
    IANA performs system administration
Users and business obtain IP addresses from ISP (Internet service provider)

## Slide 16: The OSI Model
Acronym for Open Systems Interconnection.
Model for understanding and developing network computer-to-computer communications
Developed by ISO (1980s)
Divides network communications into seven layers
  Physical, Data Link, Network, Transport, Session, Presentation, Application
  At each layer, protocols perform services unique to that layer.
  While performing those services, the protocols also interact with protocols in the layers directly above and below.

## Slide 17
Figure 2.1 Flow of data through the OSI model

## Slide 18: Application Layer
Layer 7; PDU: data
Does not include software applications however it must interact with your software applications.
Protocol functions
  Facilitates communication between software applications and lower-layer network services
  Network interprets application request
  Application interprets data sent from network

## Slide 19: Application Layer (cont’d.)
Software applications negotiate with application layer protocols
  Formatting, procedural, security, synchronization, and other requirements
  Example of Application layer protocol: HTTP

## Slide 20: Presentation Layer
Layer 6; PDU: data
Protocol functions
  Accept Application layer data
  Format data
    Understandable to different applications and hosts
Example: text encoding methods
  Presentation layer protocols perform coding and compression
Example: Presentation layer services manage data encryption and decryption

## Slide 21: Session Layer
Layer 5; PDU: data
Protocol functions
  Coordinate and maintain communications between two nodes
Session
  Connection for ongoing data exchange between two parties
    Connection between remote client and access server
    Connection between Web browser client and Web server

## Slide 22: Session Layer (cont’d.)
Functions
  Establishing and keeping alive communications link
    For session duration
  Keeping communications secure
  Synchronizing dialogue between two nodes
  Determining if communications ended
    Determining where to restart transmission
  Terminating communications

## Slide 23: Transport Layer
Layer 4; PDU: segment
Protocol functions
  Accept data from Session layer
  Manage end-to-end data delivery
  Handle flow control
Connection-oriented protocols
  Establish connection before transmitting data
  Checksum
    Unique character string allowing receiving node to determine if arriving data unit exactly matches data unit sent by source
    Further ensures data integrity

## Slide 24: Transport Layer (cont’d.)
Connectionless protocols
  Do not establish connection with another node before transmitting data
  Make no effort to ensure data is delivered free of errors
  More efficient than connection-oriented protocol
  Useful when data must be transferred quickly
Segmentation
  Breaking large data units received from Session layer into multiple smaller units called segments
  Increases data transmission efficiency

## Slide 25: Transport Layer (cont’d.)
MTU (maximum transmission unit)
  Largest data unit network will carry
  Ethernet default: 1500 bytes
  Discovery routine used to determine MTU
Reassembly
  Process of reconstructing segmented data units
Sequencing
  Method of identifying segments belonging to the same group of subdivided data

## Slide 26: Transport Layer (cont’d.)
Figure 2-2 Segmentation and reassembly

## Slide 27: Transport Layer (cont’d.)
Figure 2-3 A TCP segment

## Slide 28: Network Layer
Layer 3; PDU: packet
Protocols functions
  Translate network addresses into physical counterparts
  Decide how to route data from sender to receiver
Addressing
  System for assigning unique identification numbers to network devices
Types of addresses for nodes
  Network addresses
  Logical addresses

## Slide 29: Network Layer (cont’d.)
Packet formation
  Transport layer segment appended
    Logical addressing information
Routing
  Determine path from point A on one network to point B on another network
Routing considerations
  Delivery priorities, network congestion, quality of service, cost of alternative routes

## Slide 30: Network Layer (cont’d.)
Common Network layer protocol
  IP (Internet Protocol)
Fragmentation
  Network layer protocol (IP) subdivides Transport layer segments received into smaller packets

## Slide 31: Network Layer (cont’d.)
Figure 2-4 An IP packet

## Slide 32: Data Link Layer
Layer 2; PDU: frame (has header and trailer (FCS))
Function of protocols
  Divide data received into distinct frames for transmission in Physical layer
Frame
  Structured package for moving data
    Includes raw data (payload), sender’s and receiver’s network addresses, error checking and control information

## Slide 33: Data Link Layer (cont’d.)
Possible partial communication mishap
  Not all information received
    Corrected by error checking
  Error checking
    Frame check sequence
    CRC (cyclic redundancy check)
Possible glut of communication requests
  Data Link layer controls flow of information
    Allows NIC to process data without error

## Slide 34: Data Link Layer (cont’d.)
Two Data Link layer sublayers
  LLC (Logical Link Control) sublayer
  MAC (Media Access Control) sublayer
MAC address components
  Block ID
    Six-character sequence unique to each vendor
  Device ID
    Six-character number added at vendor’s factory
MAC addresses frequently depicted in hexadecimal format

## Slide 35: Data Link Layer (cont’d.)
Figure 2-5 The Data Link layer and its sublayers

## Slide 36: Data Link Layer (cont’d.)
Figure 2-6 A NIC’s Mac address

## Slide 37: Physical Layer
Layer 1
Functions of protocols
  Accept frames from Data Link layer
  Generate signals as changes in voltage at the NIC
Copper transmission medium
  Signals issued as voltage
Fiber-optic cable transmission medium
  Signals issued as light pulses
Wireless transmission medium
  Signals issued as electromagnetic waves

## Slide 38: Physical Layer (cont’d.)
Physical layer protocols responsibility when receiving data
  Detect and accept signals
  Pass on to Data Link layer
  Set data transmission rate
  Monitor data error rates
  No error checking
Devices operating at Physical layer
  Hubs and repeaters
NICs operate at both Physical layer and Data Link layers

## Slide 39: Applying the OSI Model
Table 2-1 Functions of the OSI layers

## Slide 40: Communication Between Two Systems
Data transformation
  Original software application data differs from application layer NIC data
    Header data added at each layer
PDUs
  Generated in Application layer
Segments
  Generated in Transport layer
  Unit of data resulting from subdividing larger PDU

## Slide 41: Communication Between Two Systems (cont’d.)
Packets
  Generated in Network layer
  Data with logical addressing information added to segments
Frames
  Generated in Data Link layer
  Composed of several smaller components or fields

## Slide 42: Communication Between Two Systems (cont’d.)
Encapsulation
  Occurs in Data Link layer
  Process of wrapping one layer’s PDU with protocol information
    Allows interpretation by lower layer

## Slide 43: Communication Between Two Systems (cont’d.)
Figure 2-7 Data transformation through the OSI model

## Slide 44: Data Frames in Network Communications
Reasons why networks split data into small pieces
  Large units of data sent across a network hamper effective communications by saturating the network
  If a sender and receiver use all the available bandwidth by sending large blocks of continuous data, other computers can’t readily communicate
  Networks can sometimes be unreliable
  Retransmission of large frames (due to errors) is inefficient

## Slide 45: Frame Specifications
Frames
  Composed of several smaller components or fields
Frame characteristic dependencies
  Network type where frames run
  Standards frames must follow
Ethernet
  Developed by Xerox
  Four different types of Ethernet frames
  Most popular: IEEE 802.3 standard

## Slide 46: Frame Specifications (cont’d.)
Token ring
  Developed by IBM
  Relies upon direct links between nodes and ring topology
  Nearly obsolete
  Defined by IEEE 802.5 standard
Ethernet frames and token ring frames differ
  Will not interact with each other
  Devices cannot support more than one frame type per physical interface or NIC

## Slide 47: IEEE Networking Specifications (cont’d.)
Table 2-2 IEEE 802 standards

## Slide 48: Summary
Standards and standard organizations
ISO’s OSI (Open Systems Interconnection) model
  Seven layers
IEEE’s Project 802
Significant IEEE 802 standards