## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 5
Topologies and Ethernet Standards

## Slide 2: Objectives
Describe the basic and hybrid LAN topologies, and their uses, advantages, and disadvantages
Describe the backbone structures that form the foundation for most networks
Compare the different types of switching used in data transmission
Explain how nodes on Ethernet networks share a communications channel
Identify the characteristics of several Ethernet standards

## Slide 3: Simple Physical Topologies
Physical topology
  Physical network nodes layout
  Depicts broad scope
  Does not specify:
    Device types
    Connectivity methods
    Addressing schemes
Fundamental shapes
  Bus, ring, star
  Hybrid

## Slide 4: Bus
Bus topology
  Single cable connects all network nodes
  No intervening connectivity devices
  One shared communication channel
Physical medium
  Coaxial cable
Passive topology
  Node listens for, accepts data
  Uses broadcast to send

## Slide 5: Bus (cont’d.)
Terminators
  50-ohm resistors
  Stop signal at end of wire
Signal bounce
  Signal travels endlessly between two network ends
One end grounded
  Removes static electricity

## Slide 6
A non terminated bus topology network
Courtesy Course Technology/Cengage Learning

## Slide 7
A terminated bus topology network
Courtesy Course Technology/Cengage Learning

## Slide 8: Bus (cont’d.)
Bus topology advantage
  Relatively inexpensive
Disadvantages
  Does not scale well
  Difficult to troubleshoot
  Not very fault tolerant

## Slide 9: Ring
Ring topology
  Node connects to nearest two nodes
  Circular network
  Clockwise data transmission
    One direction (unidirectional) around ring
  Active topology
    Workstation participates in data delivery
    Data stops at destination
  Physical medium
    Twisted pair or fiber-optic cabling

## Slide 10: Ring (cont’d.)
Drawbacks
  Malfunctioning workstation can disable network
  Not very flexible or scalable
Figure 5-2 A ring topology network
Courtesy Course Technology/Cengage Learning

## Slide 11: Star Topology
Node connects through central device
    Router or switch
Physical medium
  Twisted pair or fiber-optic cabling
Single cable connects only two devices
Advantage
  Fault tolerant
  Flexible

## Slide 12: Star (cont’d.)
Most popular fundamental layout
  Modern Ethernet networks based on star topology
1024 addressable logical network nodes maximum
Figure 5-3 A star topology network
Courtesy Course Technology/Cengage Learning

## Slide 13: Hybrid Topologies
Pure bus, ring, star topologies
  Rarely exist because too restrictive
Hybrid topology
  More likely
  Complex combination of pure topologies
  Several options

## Slide 14: Star-Wired Ring
Star-wired ring topology
  Star physical topology
  Ring logical topology
Benefit
  Star fault tolerance
Network use
  Token Ring networks
    IEEE 802.5

## Slide 15: Star-Wired Ring (cont’d.)
Figure 5-4 A star-wired ring topology network
Courtesy Course Technology/Cengage Learning

## Slide 16: Star-Wired Bus
Star-wired bus topology
  Workstation groups
    Star-connected devices
    Networked via single bus
Advantage
  Cover longer distances
  Easily interconnect, isolate different segments
Drawback
  Cabling, connectivity device expense
Basis for modern Ethernet networks

## Slide 17: Star-Wired Bus (cont’d.)
Figure 5-5 A star-wired bus topology network
Courtesy Course Technology/Cengage Learning

## Slide 18: Logical Topologies
Refers to way data transmitted between nodes
  Rather than physical layout
Does not necessarily match physical topology
Most common: bus and ring
Broadcast domain
  All nodes connected to single repeating device or switch

## Slide 19: Backbone Networks
Cabling connecting hubs, switches, routers
More throughput
Large organizations
  Fiber-optic backbone
  Cat 5 or better for hubs, switches
Enterprise-wide network backbones
  Complex, difficult to plan
Enterprise
  Entire organization
  Significant building block: backbone

## Slide 20
Figure 5-7 A simple distributed backbone
Courtesy Course Technology/Cengage Learning

## Slide 21
Figure 5-8 A distributed backbone connecting multiple LANs
Courtesy Course Technology/Cengage Learning

## Slide 22
Figure 5-9 A collapsed backbone
Courtesy Course Technology/Cengage Learning

## Slide 23
Figure 5-10 A parallel backbone
Courtesy Course Technology/Cengage Learning

## Slide 24: Variations of Physical Topologies
The major physical topologies have three typical variations or combinations
  Extended star
  Mesh
  Combination star and bus
These combinations can be used to get the most from any network

## Slide 25: Extended Star Topology
Notes: Most widely used on networks
Switch in the middle attached to hubs of star networks
That’s how Heritage network works

## Slide 26: Mesh Topology
Notes: Advantage – very fault tolerant
Disadvantage – most expensive
Every computer is attached to multiple other computers
Used in WANs, particularly high availability WANs
Internet is Mesh Topology – not entire one, just parts
Super computers are mesh technology as well

## Slide 27: Combination Star Bus Topology
Notes: A bus backbone connecting multiple hubs

## Slide 28: Hubs
In everyday use, a hub is “the center of activity”
  This definition is appropriate in network usage also
In network usage, there are a number of variations on this central theme
  Active hub
  Passive hub
  Repeating hub (just a type of active hub)
  Switching hub
Notes: Both hubs and switches can act as the center of a star topology
Agora is the hub of the college
220 the hub of CS

## Slide 29: Active Hubs
Most common type of hub today
Regenerate, or repeat, the signals
  Require electrical power to run
Generally, have many ports—eight or more
Also called multiport repeaters or repeating hubs
  Takes a signal coming in on one port
  Cleans the signal (e.g., by filtering out noise)
  Strengthens the signal
  Sends the regenerated signal out to all other ports
Drawback: require sharing the cable bandwidth among all connected stations
Notes: Sometimes called repeaters
Because they regenerate signals they need power to run
Can become a bottleneck 10 Mbps Ethernet hub with 5 devices attached is effectively 2 Mbps
Did used to be a problem, but with multimedia it is becoming one

## Slide 30: Passive Hubs
Notes: Patch panel is a passive hub
Does not amplify or regenerate, just passes things on
Just a central connection point – like box in corner of 221 lab

## Slide 31: Switches
Central connecting point in a star topology network
Does more than simply regenerate signals
Looks just like a hub, with several ports for connecting workstations in a star topology
Determines to which port the destination device is connected and forwards the message to that port
  This capability allows a switch to handle several conversations at one time, thereby providing the full network bandwidth to each device rather than requiring bandwidth sharing
Notes: Looks like a hub but is smarter

## Slide 32: Constructing a Network Layout
The first step in any network design is to evaluate the underlying requirements
  First determine how the network will be used, which often decides the topology you use
  Decide the types of devices for interconnecting computers and sites
  Finally, the type and usage level of network resources dictates how many servers you need and where to place servers
Notes: A lot of printers or file servers. Web servers, need something reliable
Usage level determines topology

## Slide 33: Selecting a Topology
Most new network designs come down to only one choice: How fast should the network be?
The physical topology will certainly be a star, and the logical topology is almost always switching
Ethernet switches are typically used on a LAN, but you might consider other logical topologies for other reasons:
  Use of legacy equipment
  Network size
  Cost restrictions
  Difficulty to run cables
Notes: Legacy equipment for FDDI rings
Hub-based for small networks
Hub may be good for a few computers being added to an existing network in a remote location (RCMP)
Wireless for add ons to existing wired network or remote locations
Tough to run cables…laptop in a house, stone building, etc

## Slide 34: Creating the Layout
Network must be documented
  Useful questions before drawing the diagram
    How many client computers will be attached?
    How many servers will be attached?
    Will there be a connection to the Internet?
    How will the building’s physical architecture influence decisions, such as whether to use a wired or wireless topology, or both?
    Which topology or topologies will you use?
Network diagram must be kept up to date

## Slide 35: Creating a Layout
Notes: How many computers are attached? 42
How many servers? 2
Is there a connection to the internet? Yes
How is physical layout affecting the topology? 2 need wireless access
What topology(ies) are used? Switching & wireless – Star Switch