## Slide 1: Wireless Networking
Chapter 8
420-A32 - Networks

## Slide 2: What is a Wireless Network?
Networks that transmit signals through the air via radio frequency (RF) waves are called wireless networks or WLANs.

## Slide 3: The Wireless Spectrum
All wireless signals are carried through the air by electromagnetic waves.
Wireless spectrum is a series of electromagnetic waves used for data and voice communication.
  Waves arranged by frequencies, from lowest to highest.
  Spectrum spans 9 KHz to 300 GHz
Each type of wireless services is associated with one area (frequency band) of the spectrum.

## Slide 4: The Wireless Spectrum

## Slide 5: Wireless vs Wired Transmission
Similarities between wireless and wired communication:
  Use same Layer 3 and higher protocols
  Same signal origination - from electrical current, travel along conductor
Differences between wireless and wired
  Signal transmission is different because no fixed path through the air.

## Slide 6: Wireless Transmission and Reception
Steps involved in wireless transmission/reception:
  1) Wireless signals originate from electrical current travelling along a conductor.
  2) Signal travels from the transmitter to an antenna, which then emits the signal into the air.
  3) Signal propagates through the air until it reaches its destination.
  4) At the destination, another antenna accepts the signal, and a receiver converts it back to electrical current.

## Slide 7: Wireless Transmission and Reception

## Slide 8: Antennas
An antenna is used for signal transmission and reception.
  The same frequency is required on each antenna, which means they share the same channel.
Each type of wireless service requires an antenna designed specifically for that service.
Radiation pattern = relative strength over three-dimensional area

## Slide 9: Antennas
A directional antenna issues wireless signals along a single direction.
  Used in a point to point link.
Omnidirectional antenna issues and receives wireless signals with equal strength and clarity in all directions.
  Used when many receivers must pick up the signal.
  TV and radio stations.
Range = geographical area that an antenna can reach.
  Receivers must be in range.

## Slide 10: Signal Propagation
Ideally a wireless signal would travel in a straight line from transmitter to receiver.
  called LOS (line-of-sight) propagation
However there are obstacles that affect signal travel and the signal must pass through or absorb the obstacle.
  Signal problems:
    Reflection: bounce signal back to source
    Diffraction: splits signal into secondary waves
    Scattering: reflection of signal in multiple different directions

## Slide 11: Signal Propagation
As a result of these reflection, diffraction and scattering, wireless signals follow a number of different paths to their destination.
  Called multipath signals
Multipath advantage:
  Better chance of reaching destination
Multipath disadvantage:
  Signal delay

## Slide 12: Multipath Signal Propagation

## Slide 13: Signal Degradation
When signals run into obstacles, the signal will experience fading as a result of the electromagnetic energy scattered, reflected, diffracted.
  Received signal is lower than the transmitted signal’s strength.
Attenuation - signal weakens as it moves away from transmission antenna
  Correcting signal attenuation requires a repeater.
Noise (EMI) is biggest problem with signals because the air contains so many electromagnetic waves.

## Slide 14: Wireless Spectrum Use
Narrowband
  Transmitter concentrates signal energy at single frequency, very small frequency range
Broadband
  Relatively wide wireless spectrum band
  Higher throughputs than narrowband
Spread-spectrum
  Multiple frequencies used to transmit signal
  Offers security

## Slide 15: Fixed versus Mobile
Each type of wireless communication falls into either
  Fixed
  Mobile
In fixed systems the location of the transmitter and receiver do not move.
  Advantage
    No wasted energy issuing signals
    More energy used for signal itself
In mobile systems the receiver is located anywhere within transmitter’s range.
    Receiver can roam

## Slide 16: WLAN Architecture
Ad hoc WLAN
  Wireless nodes (stations) transmit directly to each other using wireless NICs.
    There is no intervening connectivity device
  Poor performance
    Many spread out users, obstacles block signals

## Slide 17: An Ad hoc WLAN

## Slide 18: WLAN Architecture
An access point (AP) is a device that accepts wireless signals from multiple nodes and retransmits signals to network.
  Base stations, wireless routers, wireless gateways
Infrastructure WLAN
  Stations communicate with access point and not directly with each other.
  Access point requires sufficient power, strategic placement
WLAN may include several access points
  Dependent upon number of stations; max varies: 10-100

## Slide 19: An Infrastructure WLAN

## Slide 20: WLAN Architecture
Mobile networking allows roaming wireless nodes
  Range dependent upon wireless access method, equipment manufacturer, office environment
    Access point range: 300 feet maximum
Can connect two separate LANs
  Fixed link, directional antennas between two access points
    Allows access points 1000 feet apart
Support for same protocols, operating systems as wired LANs
  Ensures compatibility

## Slide 21: WLAN Interconnection

## Slide 22: IEEE 802.11 WLANs
Wireless standards vary by frequency, methods of signal and geographic range.
Wi-Fi (wireless fidelity) standards
  802.11b, 802.11a, 802.11g, 802.11n
  Share characteristics
    Half-duplexing
    CSMA/CA access method
    frame format

## Slide 23: 802.11 Access Method
802.11 MAC services
  Append 48-bit (6-byte) physical addresses to frame
    Identifies source, destination
Same physical addressing scheme as 802.3
  Allows easy combination
Wireless devices
  Not designed for simultaneous transmit, receive
  Cannot quickly detect collisions
  Use different access method

## Slide 24: 802.11 Access Method
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Minimizes collision potential
  Uses ACK packets to verify every transmission
    Requires more overhead than 802.3
    Real throughput less than theoretical maximum
RTS/CTS (Request to Send/Clear to Send) protocol
  Ensure packets not inhibited by other transmissions
  Efficient for large transmission packets
  Further decreases overall 802.11 efficiency

## Slide 25: 802.11 Association
Association is a packet exchange between a computer and an access point to gain Internet access.
Scanning
  Surveying surroundings for access point
  Active scanning transmits special frame called a probe.
  Passive scanning listens for special signal called a beacon frame.

## Slide 26: 802.11 Association
SSID (service set identifier)
  Unique character string identifying access point
    In beacon frame information
  Configured in access point
  Better security, easier network management
BSS (basic service set)
  Station groups sharing access point
  BSSID (basic service set identifier)
    Station group identifier

## Slide 27: Association
ESS (extended service set)
  Access point group connecting same LAN
    Share ESSID (extended service set identifier)
  Allows roaming
    Station moving from one BSS to another without losing connectivity
When several access points are detected:
  Select strongest signal, lowest error rate
  Poses security risk
    Powerful, rogue access point

## Slide 28: Network with Single BSS

## Slide 29: Network with Multiple BSSs Forming an ESS

## Slide 30: Association
ESS with several authorized access points
  Must allow station association with any access point
    While maintaining network connectivity
Reassociation
  Mobile user moves from one access point’s range into another’s range
  Occurs by simply moving, high error rate
Stations’ scanning feature
  Used to automatically balance transmission loads
    Between access points

## Slide 31: Basic 802.11 Frame
3 Frame types:
  Management – used for association and reassociation
    i.e. Beacon frames, probe frames
  Control – related to medium access and data delivery.
    i.e. ACK frames
  Data – used to carry data
Frames contain 4 address fields
  source address
  destination address
  transmitter address – refer to the access point
  receiver address – refer to the access point

## Slide 32: 802.11 Standards
802.11b
  DSSS (direct-sequence spread spectrum) signaling
  Oldest, least expensive, being replaced by 802.11g
802.11a
  Released after 802.11b
  More expensive, least popular
802.11g
  As affordable as 802.11b but provides better throughput
802.11n – Standardized in Sept 2009
  Provides much higher effective throughput than others
  MIMO (multiple input-multiple output) - Multiple access point antennas may issue signal to one or more receivers

## Slide 33: Bluetooth Networks
Ericson’s original goals
  Wireless technology compatible with multiple devices
  Require little power
  Cover short ranges
Bluetooth is a mobile wireless networking standard using FHSS (frequency hopping spread spectrum) RF signaling.
  2.4-GHz band.
  Used by home networks.

## Slide 34: Bluetooth Networks
Version 1.1
  Effective throughput: 723 Kbps
  10 meter node difference
  Designed for PANs (personal area networks)
Version 2.0 (2004)
  Different encoding schemes
    2.1-Mbps throughput
  30 meters node difference
  Usage: cellular telephones, phone headsets, computer peripherals, PDAs

## Slide 35: Summary of WLAN Standards

## Slide 36: Implementing a WLAN
Designing a small WLAN
  Home, small office
Formation of larger, enterprise-wide WANs
Installing and configuring access points and clients
Implementation pitfalls
  Avoidance
Material applies to 802.11b and 802.11g
  Most popular

## Slide 37: Designing a Smaller WLAN
Most home and small office WLANs depend on a single access point.
  Combine with switching, routing functions
  Connects wireless clients to LAN
  Acts as Internet gateway
Access point WLAN placement considerations
  Should be centrally located to provide reliable wireless service at any location.
  Obstacles
    Type, number between access point and clients

## Slide 38: Home or Small Office WLAN

## Slide 39: Designing a Larger WLAN
Larger WLANs
  Need to determine the appropriate number of access points.
  Systematic approach to access point placement
Site survey
  Assesses client requirements, facility characteristics, coverage areas
  Determines access point arrangement ensuring reliable wireless connectivity within given area.
  Proposes access point testing
    Testing wireless access from farthest corners

## Slide 40: Designing a Larger WLAN
Install access points
  Must belong to same ESS, share ESSID
Enterprise-wide WLAN design considerations
  How wireless LAN portions will integrate with wired portions

## Slide 41: Enterprise-wide WLAN

## Slide 42: Configuring Wireless Clients
Configuration varies from one client type to another
Windows XP client WLAN configuration
  Use graphical interface
Linux clients wireless interface configuration
  Use graphical interface
  iwconfig command-line function
    View, set wireless interface parameters
Should change SSID and administrator password.

## Slide 43: Output from iwconfig command

## Slide 44: Avoiding Pitfalls
Access point versus client configurations
  SSID mismatch
  Incorrect encryption
  Incorrect channel, frequency
  Standard mismatch (802.11 a/b/g/n)
Incorrect antenna placement
  Verify client within 330 feet
Interference
  Check for EMI sources

## Slide 45: Wireless WANs and Internet Access
Wireless broadband
  Latest wireless WAN technologies
  Specifically designed for:
    High-throughput, long-distance digital data exchange

## Slide 46: 802.11 Internet Access
Access points: 802.11b or 802.11g access methods
Hot spots
  Places with publicly available wireless Internet access
  Free or subscription
Hot spot subscription Internet access
  Log on via Web page
  Client software managing client’s connection
    Network log on, secure data exchange
    Added security: accept connection based on MAC address
Accept user’s connection based on MAC address

## Slide 47: 802.16 (WiMAX) Internet Access
WiMAX (Worldwide Interoperability for Microwave Access)
    Improved mobility, QoS characteristics
    Digital voice signals, mobile phone users
Functions in 2 and 66 GHz range
  Licensed, nonlicensed frequencies
Line-of-sight paths between antennas
  Throughput potential maximized
Non-line-of-sight paths
  Exchange signals with multiple stations at once

## Slide 48: 802.16 (WiMAX) Internet Access
Two distinct advantages over Wi-Fi
  Much greater throughput (70 Mbps)
  Much farther range (30 miles)
Appropriate for MANs and WANs
Highest throughput achieved over shortest distances between transceivers
Possible uses
  Alternative to DSL, broadband cable
  Well suited to rural users
  Internet access to mobile computerized devices
  Residential homes

## Slide 49: WiMAX Residential Service

## Slide 50: WiMAX Antenna
WiMAX residential antenna
WiMAX service provider’s antenna

## Slide 51: 802.16 (WiMAX) Internet Access
Metropolitan area installation
  Home antenna, connectivity device eliminated
WiMAX MANs
  Extensive connectivity
  Download data rates faster than home broadband connection
  Shared service
    Apportioned bandwidth
Drawback
  Expensive

## Slide 52: Satellite Internet Access
Used to deliver:
  Digital television and radio signals
  Voice and video signals
  Cellular and paging signals
Provides homes and businesses with Internet access

## Slide 53: Satellite Orbits
Geosynchronous orbit
  Satellites orbit the Earth at the same rate as the Earth turns
  Downlink
    Satellite transponder transmits signal to Earth-based receiver
  Typical satellite
    24 to 32 transponders
    Unique downlink frequencies
LEO (low Earth orbiting) satellites
  Orbit Earth with altitude 100 miles to 1240 miles
  Not positioned over equator

## Slide 54: Satellite Communication

## Slide 55: Satellite Orbits
MEO (medium Earth orbiting) satellites
  Orbit Earth 6000 to 12,000 miles above surface
  Not positioned over equator
    Latitude between equator and poles
  Advantage
    Cover larger Earth surface area than LEO satellites
    Less power, less signal delay than GEO satellites
Geosynchronous orbiting satellites most popular for satellite Internet access

## Slide 56: Satellite Internet Services
Subscriber
  Small satellite dish antenna, receiver
  Exchanges signals with provider’s satellite network
Satellite Internet access service
  Dial return arrangement (asymmetrical)
    Receives Internet data via downlink transmission
    Sends data to satellite via analog modem connection
  Satellite return arrangement (symmetrical)
    Send, receive data to and from Internet using satellite uplink and downlink

## Slide 57: Dial Return Satellite Internet Service