## Slide 1: Wireless Network Security
420-A32 Networks

## Slide 2: Default security
By default 802.11 does not offer any security.
In addition, most access points do not require that the user authenticate before communicating with the AP.
The only requirement is that it knows the AP’s SSID which most routers broadcast by default.
This creates a very insecure environment using strictly the default settings.

## Slide 3: Implementing Wireless Security
Attackers who drive around looking for wireless LANs to intercept are called wardrivers
Some common wireless security methods
  SSID
  Admin Password
  Wired Equivalency Protocol (WEP)
  Wi-Fi Protected Access (WPA)
  MAC address filtering
You should also set policies: limit AP signal access, change encryption key regularly, etc.
Notes: Service set identifier – label given to your access point. Clients must configure their NIC to talk to that SSID
- if you broadcast people know what the id is
WEP – attacker only sees gibberish
WiFi Protected Access – more difficult to hack, WEP static key, WPA changes it
802.11i – WPA 2 – advanced encryption handling and secure method of handling keys
MAC address filtering – most secure, only agreed to Wireless devices can connect to the network

## Slide 4: Change Default Administrator Passwords (and Usernames)
At the core of most Wi-Fi home networks is an access point or router.
To set up these pieces of equipment, manufacturers provide Web pages that allow owners to enter their network address and account information.

## Slide 5: Change Default Administrator Passwords (and Usernames)
These Web tools are protected with a login screen (username and password) so that only the rightful owner can do this.
However, for any given piece of equipment, the default logins provided are simple and very well-known to hackers on the Internet. Change these settings immediately.

## Slide 6: Turn on (Compatible) WPA / WEP Encryption
All Wi-Fi equipment supports some form of encryption.
Encryption technology scrambles messages sent over wireless networks so that they cannot be easily read by humans.
Several encryption technologies exist for Wi-Fi today.

## Slide 7: Turn on (Compatible) WPA / WEP Encryption
Naturally you will want to pick the strongest form of encryption that works with your wireless network.
However, the way these technologies work, all Wi-Fi devices on your network must share the identical encryption settings.
Therefore you may need to find a "lowest common demoninator" setting.

## Slide 8: WEP
WEP is an older network security method that is still available to support older devices, but it is no longer recommended.
When you enable WEP, you set up a network security key.
This key encrypts the information that one computer sends to another computer across your network.
However, WEP security is easy to crack using freely available software on the internet so if possible, avoid this method.

## Slide 9: WEP
The reason you may still see WEP wireless protection being used is:
  Improper setup by administrator
  This is the only security protocol that all devices using the network supports
  Wireless access device offers no other options

## Slide 10: WPA
WPA encrypts information, and it also checks to make sure that the network security key has not been modified.
WPA also authenticates users to help ensure that only authorized people can access the network.

## Slide 11: WPA
There are two types of WPA authentication:
  WPA and WPA2.
WPA is designed to work with all wireless network adapters, but it might not work with older routers or access points.
WPA2 is more secure than WPA, but it will not work with some older network adapters.

## Slide 12: WPA
WPA is designed to be used with an 802.1X authentication server, which distributes different keys to each user.
This is referred to as WPA-Enterprise or WPA2-Enterprise.
It can also be used in a pre-shared key (PSK) mode, where every user is given the same passphrase.
  This is referred to as WPA-Personal or WPA2-Personal.

## Slide 13: WPA
While WPA is more secure than WEP the PSK mode has been cracked and is not longer deemed secure.
The other versions of WPA are susceptible to a brute force or dictionary attack and can be cracked this way if your encryption key is in the dictionary or very simple.
These modes have been know to be cracked in one day when simple keys were being used.

## Slide 14: WPA
While WPA is more secure than WEP the PSK mode has been cracked and is not longer deemed secure.
The other versions of WPA are susceptible to a brute force or dictionary attack and can be cracked this way if your encryption key is in the dictionary or very simple.
These modes have been know to be cracked in one day when simple keys were being used.

## Slide 15: recommendation
Use the highest encryption standard supported by your devices.
Use a strong encryption key with a mix of letters, numbers, and special characters.
The longer the key, the longer it will take a hacker to capture it using a brute force attack.

## Slide 16: Change the default SSID
Access points and routers all use a network name called the SSID.
Manufacturers normally ship their products with the same SSID set.
For example, the SSID for Linksys devices is normally "linksys“ and D-Link routers usually use “dlink.”

## Slide 17: Change the default SSID
True, knowing the SSID does not by itself allow your neighbors to break into your network, but it is a start.
It allows the hacker to determine all the defaults for your router.
This gives them a variety of attacks to try including:
  Using the default gateway address and admin password to gain access to your router’s administration menu.
  Using any vulnerabilities that may be particular to that device.
  Attacking any ports that are known to be vulnerable on that type of device.

## Slide 18: Change the default SSID
More importantly, when someone finds a default SSID, they see it is a poorly configured network and are much more likely to attack it.
Change the default SSID immediately when configuring wireless security on your network.

## Slide 19: Enable mac address filtering
Each piece of Wi-Fi gear possesses a unique identifier called the physical address or MAC address.
You can set your router to only accept connections from devices with known MAC addresses.

## Slide 20: Enable mac address filtering
If you enable this option you must manually enter the MAC address of all allowable devices in the admin panel of your router.
Each time a new device needs to join the network, you will have to make the manual MAC address entry.

## Slide 21: Enable mac address filtering
This is more time intensive as each new device needs to be manually entered into the admin section of the router.
Furthermore, new devices cannot add themselves to the network using only the user password, since the admin password is required to add their device to the list.

## Slide 22: Enable mac address filtering
This does provide more protection however since devices whose MAC address is unknown will be denied access even if they know the encryption password.
This is not fool proof however, since hackers can spoof their MAC address and gain entry if they know both the user password and the MAC address of a authorized device.

## Slide 23: Enable mac address filtering
This does provide more protection however since devices whose MAC address is unknown will be denied access even if they know the encryption password.
This is not fool proof however, since hackers can spoof their MAC address and gain entry if they know both the user password and the MAC address of a authorized device.

## Slide 24: Disable remote administration
Disabling remote administration privileges is a great way to close the door on anyone looking to access your security settings.
However it is often enabled by default.
The option should be located in your router’s administrative settings and requires all security modifications to be changed directly through a wired connection to your router.

## Slide 25: Change your routers IP address
By changing your router’s IP address, you make it more difficult for a hacker to find the address of the router’s admin panel.
This also creates a new address range for your network.
Combine this with turning off DHCP service on your router to make it more difficult for a hacker to find your network IP address range.

## Slide 26: Use static IP addresses
Most home networkers gravitate toward using dynamic IP addresses.
DHCP technology is indeed easy to set up.
Unfortunately, this convenience also works to the advantage of network attackers, who can easily obtain valid IP addresses from your network's DHCP pool.

## Slide 27: Use static IP addresses
Turn off DHCP on the router or access point, set a fixed IP address range instead, then configure each connected device to match.
This means that the hacker will have to figure out your networks IP address range so that they can get a valid IP in this range.

## Slide 28: Use static IP addresses
For extra precaution, use a private IP address range to prevent computers from being directly reached from the Internet in case a particularly determined hacker makes his way through your firewall. This is the list of private IP addresses that you can use.

## Slide 29: Keep your firewall enabled
Modern network routers contain built-in firewall capability, but the option also exists to disable them.
Ensure that your router's firewall is turned on.
For extra protection, consider installing and running personal firewall software on each computer connected to the router.

## Slide 30: Close any unused ports on your router
Common ports attacked by hackers are:
TCP port 21 - FTP (File Transfer Protocol)
TCP port 22 – SSH (Secure Shell)
TCP port 23 - telnet
TCP port 25 - SMTP (Simple Mail Transfer Protocol)
TCP and UDP port 53 - DNS (Domain Name System)
TCP port 443 - HTTP (Hypertext Transport Protocol) and HTTPS (HTTP over SSL)
TCP port 110 - POP3 (Post Office Protocol version 3)
TCP and UDP port 135 - Windows RPC
TCP and UDP ports 137–139 - Windows NetBIOS over TCP/IP
TCP port 1433 and UDP port 1434 – Microsoft SQL Server

## Slide 31: Close any unused ports on your router
In the router’s admin panel you can close any of these ports that you know you do not need.
This will make it more difficult for hacker’s to attack your network.

## Slide 32: Close any unused ports on your router
Note that some software opens ports on your router without your knowledge or asks you to open ports.This provides a new entrance for hackers.
Be sure to close all these ports if you do not need them:
  If you uninstall the software
  If you will not be using the software for a while
You can always reopen the ports later as required.

## Slide 33: Position your access points carefully
Wi-Fi signals normally reach to the exterior of a home.
A small amount of signal leakage outdoors is not a problem, but the further this signal reaches, the easier it is for others to detect and exploit.

## Slide 34: Position your access points carefully
Wi-Fi signals often reach through neighboring homes and into streets, for example.
When installing a wireless home network, the position of the access point or router determines its reach.
Try to position these devices near the center of the home rather than near windows to minimize leakage.

## Slide 35: Turn off your wireless network
The ultimate in wireless security measures, shutting down your network will most certainly prevent outside hackers from breaking in!
While impractical to turn off and on the devices frequently, at least consider doing so during travel or extended periods offline.
If all of your devices are wired with the occasional wireless user, check for an option to turn off the wireless signal while leaving the router’s wired ports functional.